Incubator for Microplates——DH400

Description:

DH400 Incubator for Microplates is a kind of microprocessor controlled and PID controlled incubator. It is compact, versatile, reliable and easy to use. It is mainly used in elisa plates(96/384 wells) or tissue culture plates(24/48/96 wells, etc) for samples cultivation of incubation.

Features:

- LCD display.

- Easy to operate with one-touch knob.

- Microprocessor and temperature controlled with good liner, small fluctuations.

- Double heating system ensures the stability of incubation.

- Internal power supply provided is UL, CSA and CE approved.

Applications:

Сytochemistry — for in situ reactions

Immunochemistry — for immunofermentative reactions

Biochemistry — for enzyme and protein analysis

Molecular biology — for micro array analysis

Parameters:

| Type Parameters | DH400 |
| --- | --- |
| Temp. control range | RT.+5℃ ~80℃ |
| Time range | 1min ~ 99h59min |
| Temp. accuracy | ≤±0.5℃ |
| Display accuracy | 0.1℃ |
| Temp. uniformity | ≤±0.5℃ |
| Heating time | ≤10min(from 25℃ to 80℃) |
| Max. height of plate | 22mm |
| Capacity | 2plates |
| Power | 120W |
| Voltage | AC220V or AC110V, 50/60Hz |
| Dimension(mm) | 280×270×140 |
| Weight(kg) | 4.0 |