Sample Concentrator—ND100-2

Description:

ND100-2 sample concentrator is with microprocessor controlled and PID fuzzy controlled technique. Instead of traditional water bath device, the heat-conducting medium is high purity aluminum. The Test tubes are held in block, and blowing a large number of samples at one time.

Can used in residue analysis, commodity inspection, food, environment, pharmacy and biological product and other industries.

Features:

- High precision and wide range of tamp control.

- Blowing a large number of samples at one time.

- Blowing each sample independently.

- Amount of airflow can be adjusted.

- Easy operation; safe and reliable to use.

Applications:

- Analysis of pesticide residues: vegetables, fruits, cereals, plant tissue.

- Environmental analysis: such as drinking water, groundwater and polluted water samples.

- Biological analysis: such as hormone analysis, sample preparation of liquid phase and gas phase and mass spectrometry analysis.

- Food and beverage: such as milk, wine, beer, etc.

- Pharmaceutical drug testing: such as traditional Chinese medicine pharmaceutical, drug screening.

Parameters:

| Model | ND100-2 |
| --- | --- |
| Temp range | RT.+5(C -160(C |
| Temp accuracy | ±0.5℃(@40℃) |
| Temp accuracy | ±1℃(@120℃) |
| Temp uniformity | ±0.5℃ |
| Display accuracy | 0.1℃ |
| Time range | 1min-99h59min/∞ |
| Heating time | ≤15min(from 25℃ to 160℃) |
| Needle length | 150mm |
| Nitrogen flow rate | 15L/min |
| Nitrogen pressure | 0.02Mpa(Gas needle≤16pcs) 0.05Mpa(Gas needle＞16pcs) |
| Block quantity | 2 |
| Max power | 500W |
| Voltage | AC220V or AC110V, 50/60Hz |
| Dimension(mm) | 260x220x450 |
| Weight(kg) | 7.5 |

Optional Blocks:

| Type | Description | Type | Description |
| --- | --- | --- | --- |
| MD03 | 24x10mm | MD09 | 12x20mm |
| MD04 | 24x12mm | MD10 | 8x26mm |
| MD05 | 24x13mm | MD11 | 4x28mm |
| MD06 | 16x15mm | MD12 | 3x40mm |
| MD07 | 16x16mm | MD15 | 24x1.5ml(centrifuge tube) |
| MD08 | 12x19mm | MD16 | 24x2.0ml(centrifuge tube) |